# SUBJECT: ET 26 NEXS Docking Switch Wiring Modification

# SERVICE BULLETIN REF.  06/0102

DATE: January 2006

We have discovered a problem with the ET 26 & 30 NEXS machines out in the field; an operator has found that you can defeat the PTO/HANDBRAKE interlock.  To overcome this problem minor a wiring change is required on all machines in service.

The wiring change is as follows: - using wiring diagram nos see note below.

1. The normally open wire of the docking switch (core no 1) VDL terminal strip no 5 found in the pedestal junction box see photograph below

Note: - For Vauxhall Vivario use wiring diagram no 1160-57 revision “c”

For Mercedes Sprinter use wiring diagram no 1160-62 revision “b”

For Ford Transit use wiring diagram no 1160-53 revision “b”

Remove terminal wire no 5 on the left hand side of the terminal strip and check for voltage using a voltmeter, the wire to be moved is the one without voltage on it when checked with the voltmeter, the wire no 5 that has voltage on it needs to be refitted to terminal position no 5.

When you have correctly identified the wire coming from the docking switch (core no 1) renumber this to terminal no 4 and fit the wire to position no 4 of the terminal strip

If you have any questions, or if further information is required, please contact the Versalift Technical Help Line on 01536 721010

# Text boxes

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

SERVICE

BULLETIN

Versalift Distributors (UK) Ltd 1 Altendiez Way Latimer Park Burton Latimer Northants. NN15 5YZ

### Tel. 01536 721010          Fax 01536 721110         Email: admin@versalift.co.uk

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT