# TO:  All Versalift Users

# SUBJECT: Emergency Motor Operation

# SERVICE BULLETIN REF.  05/0202

DATE: August 2004

It has been found that if the machine is deliberately operated incorrectly it is possible to defeat the interlock system and operate the booms without deploying the stabilisers.  To prevent this happening in the future an emergency motor interlock relay has been introduced on production on all machines produced after 1 April 04.

It is strongly recommended that this extra relay is fitted to all earlier machines to ensure that the boom stabiliser interlock can not be defeated.  The relay is available with fitting instructions from Versalift Distributors (UK) Ltd Parts Department.

This bulletin is for technical information purposes only and does not constitute authority for mandatory replacement of parts or warranty claim submission.

If you have any questions, or if further information is required, please contact the Versalift Technical Help Line on 01536  721010

# Text boxes

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

SERVICE

BULLETIN

Versalift Distributors (UK) Ltd  1 Altendiez Way  Latimer Park  Burton Latimer  Northants. NN15 5YZ

### Tel. 01536 721010          Fax 01536 721110         Email: admin@versalift.co.uk

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

PLEASE NOTE THE SERVICE DEPT FAX NUMBER

01536 721110