# TO:  All Versalift Users

# SUBJECT: Emergency Motor Operation

# SERVICE BULLETIN REF.  06/0801

DATE: August 2006

A number of cases of the emergency pump failing to operate have been reported, which on investigation have been found to be caused by the emergency motor solenoid sticking.  Investigation has shown that the solenoids almost invariable stick due to lack of use.

It is important that the emergency motor is tested from both ground and bucket controls as part of the routine daily checks carried out on the machine.

During this check the it is only necessary to operate the emergency motor for a few seconds from both control positions and as well as being an important part of the daily checks will ensure that the solenoid does not stick.

This bulletin is for technical information purposes only and does not constitute authority for mandatory replacement of parts or warranty claim submission.

If you have any questions, or if further information is required, please contact the Versalift Technical Help Line on 01536  721010

# Text boxes

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

SERVICE

BULLETIN

Versalift Distributors (UK) Ltd  1 Altendiez Way  Latimer Park  Burton Latimer  Northants. NN15 5YZ

### Tel. 01536 721010          Fax 01536 721110         Email: admin@versalift.co.uk

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

PLEASE NOTE THE SERVICE DEPT FAX NUMBER

01536 721110