# TO:  All Versalift Users

# SUBJECT: Flyboom pivot bearings

# SERVICE BULLETIN REF.  05/0502

DATE: April 05

On a number of recent occasions it has been found that the bolts securing the bearing housings on the top and bottom flyboom pivots have been allowed to remain loose for a considerable period of time.  We must point out that these bolts are considered to be a critical fastener and are marked with sentry seal on production.  This therefore requires these bolts to be part of the operator’s daily inspection and a careful check during all routine services to ensure that they are retightened if they should become loose.

Failure to ensure that these securing bolts are tight could lead to fretting between the bearing housing and the flyboom structure as well as elongation of the bolt holes.

This bulletin is for technical information purposes only and does not constitute authority for mandatory replacement of parts or warranty claim submission.

If you have any questions, or if further information is required, please contact the Versalift Technical Help Line on 01536  721010

# Text boxes

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

SERVICE

BULLETIN

Versalift Distributors (UK) Ltd  1 Altendiez Way  Latimer Park  Burton Latimer  Northants. NN15 5YZ

### Tel. 01536 721010          Fax 01536 721110         Email: admin@versalift.co.uk

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

PLEASE NOTE THE SERVICE DEPT FAX NUMBER

01536 721110