# TO:  All Versalift Users

# SUBJECT: Bucket Levelling System

# SERVICE BULLETIN REF.  04/0201

DATE: February 2004

As part of our continued product enhancement programme we have introduced changes to the cage levelling system on all new machines.

- The cage-levelling switch at the ground controls has been repositioned inside the control box to prevent unauthorised operation of the cage levelling system.  It is recommended that this upgrade is fitted to earlier machines, the next time the machine is undergoing service or repair.  A kit is available to carry out this upgrade from Versalift Distributors (UK) Ltd.  If this upgrade is not fitted it is important that a suitable safe system of work is employed to prevent unauthorised operation of the ground control cage trim switch, and that there is a rescue system in place.

- The operational speed of the cage trimming system has been reduced to give a smoother operation.  It is recommended that this upgrade is fitted the next time the machine is undergoing service or repair.  This modification can be carried out by our engineers while carrying out routine services and thorough examinations.

This bulletin is for technical information purposes only and does not constitute authority for mandatory replacement of parts or warranty claim submission.

If you have any questions, or if further information is required, please contact the Versalift Technical Help Line on 01536  721010

# Text boxes

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

SERVICE

BULLETIN

Versalift Distributors (UK) Ltd  1 Altendiez Way  Latimer Park  Burton Latimer  Northants. NN15 5YZ

### Tel. 01536 721010          Fax 01536 721110         Email: admin@versalift.co.uk

## IMPORTANT     IMPORTANT     IMPORTANT    IMPORTANT     IMPORTANT

PLEASE NOTE THE SERVICE DEPT FAX NUMBER

01536 721110