M20 X 60 Pedestal Bolts

Following on from recent incidents where Pedestal Bolt heads were snapping, please be aware of the findings:

All of the failed bolts were found to be from the same batch supplied to Versalift between December 2013 and June 2014. These bolts are all brand stamped on the head with ‘TY’.

To prevent further failings, and as a precautionary measure – all M20 X 60 Pedestal Bolts with TY stamped in to them should be changed on our routine LOLER Inspections.

# Text boxes

## VERSALIFT